## Slide 1: Build your own Arduino uno shield Session 02

## Slide 2: Last week
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
You learnt to:
  Breadboard & connect modules to the Arduino Uno
  Basic program to control the LEDs on the dot matrix
  Set up EAGLE directories
  Add components in EAGLE

## Slide 3: THIS week
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 4: Waypoints
Preparing the board
Board Dimensions
Part Placement
Good parts placement is half the battle won
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Change grid units to mm
Change grid units to 10 mil
Setting up route parameters
Eg. (Bend Style, Width, Via shape, via drill size)
Trace width of 32 mil
Route lines in parallel on bottom layer
Trace width of 16 mil
Route lines on top layer
Logo
Labels
Schematic Drawing
GND Planes
Polygons, signals and ratsnest

## Slide 5: Adding components
Symbol Preview
Footprint Preview

## Slide 6
Symbol Preview
(DOES NOT CHANGE)
Footprint Preview
(CHANGES)
3mm
5mm
10mm

## Slide 7
Symbol Preview
Footprint Preview

## Slide 8
Add components
Add components



Let’s start with the Arduino Uno Reference
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 9
Add power symbols
Add components
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
Add 5V and GND

## Slide 10
Connect the power lines to the Arduino
Net
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
Use the net wire to connect the symbol
from point to point

## Slide 11
Your first EAGLE circuit
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
Try doing this by yourself
“Hello World” EAGLE style

## Slide 12
Understanding how .sch & .Brd are connected
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
EAGLE WALKTHROUGH
LIVE DEMO TIP :
Using move to auto-magically generate net wire connections.
Using copy to make copies of existing components (eg. GND) to add to the circuit.
Net wire in .sch  air wire in .brd
Notes: Set up dual window layout
Do a live demo of the previous assignment.
Showcase the following tips
Using move to automagically generate net wire connections.
Using copy to make copies of gnd to add to the circuit.
Net wire in sch = air wire in brd

## Slide 13
Let’s try that out with the push buttons
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
TIP :
You can make connections by naming the net wires as well.
Let’s try that out!

## Slide 14
New tips, and here comes the matrix
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
EAGLE WALKTHROUGH
Notes: New command:
Mirror
Move
Invoke power

## Slide 15
BY THIS TIME, Your Arduino should have the following pin outs
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 16
PAndemic Pindemic Breakout
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
(Optional )
For rtc
Notes: This is where you might wanna breakout other pins as well if you’re planning to add in your own sensors/ general pin outs for future use

## Slide 17
Error Checking (ERC)
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
Common Mistakes
Error Descriptions, what they mean, and how to solve it
ERC
ERC = Electrical Rule Check
This command is used to test schematics for electrical errors.

## Slide 18
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
Great job getting here
Let’s take a break

## Slide 19: Waypoints
Preparing the board
Board Dimensions
Part Placement
Good parts placement is half the battle won
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Change grid units to mm
Change grid units to 10 mil
Setting up route parameters
Eg. (Bend Style, Width, Via shape, via drill size)
Trace width of 32 mil
Route lines in parallel on bottom layer
Trace width of 16 mil
Route lines on top layer
Logo
Labels
Schematic Drawing
GND Planes
Polygons, signals and ratsnest

## Slide 20
Components situated
OUTSIDE of the board
Board Dimension
Defined with Line of width 0
on Dimension Layer
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 21
Select Grid

Change grid units to mm

Select mm

Change size to 1

Select “On” to display grid lines

Click OK
TIP : Working with grid units in mm is great for parts placement to have a sense of measurement
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 22
Select Move

Parts placement :
Good parts placement is half the battle won
Since we’ve already helped you with the quick start for the Arduino layout & board dimensions, the next thing to place would be the dot matrix.
TIP : Use air-wires to help indicate the orientation and location of parts that provides the shortest path to route between each other.
Click on “Route” if the air-wires are not showing up. Alternatively, enable the unrouted (19) layer.
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

Select the origin of the footprint
Align the dot matrix to the center using the blue
Arduino line as reference

EAGLE WALKTHROUGH
Notes: EAGLE Live demo

## Slide 23
TIP : While deciding on where to place the parts, keep in mind that it should not block the connection to other components/ other components are not blocking it.
Eg. OK to place shift registers underneath the dot matrix module.
NOT OK to place the push buttons or LEDs underneath the dot matrix module.
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 24
Select Grid

Change grid units to mil
(Unit of measurement for very thin objects - Equal to 1⁄1000 of an inch )

Change size to 10

Click OK
TIP: Working with grid units in mil is great for routing (dealing with a number like 10 mil is so much friendlier than 0. 25mm)

Select mil
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 25
Select Route

Preparing to route
Some things you need to know
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 26
Route power lines first
TIP : Route power lines on the bottom layer of the board, route all signal traces for components on the top layer.
Always run the power lines (+ and -) in parallel to each other.
Select Route

Select Bottom Layer


Select 32

Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 27
Route power lines first
TIP : Route power lines on the bottom layer of the board, route all signal traces for components on the top layer.
Select air wire at GND of Arduino Board

Click to place a bend point before continuing

Click on centre of GND pin to complete trace route
Line should automatically disappear

Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 28
Route power lines first
TIP : As much as possible, avoid daisy chaining the power lines from part-to-part.
GND
5V
“Always run the power lines (+ and -) in parallel to each other.”
Repeat the steps the other 5V and GND lines.
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
TIP :
Use the grid lines to gauge minimum clearance between the traces.
(That’s the reason why we use 10mil)

## Slide 29
ROUTE SIGNAL LINES
Select top Layer

Select 16 mil

TIP : Is another line blocking? Use Vias!
Eg. SMD on top layer of board needs to connect to a GND on the bottom layer of the board, route a top layer trace from the LED, and select Bottom Layer and continue routing to a GND pin. A via will automatically appear!
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 30
GROUND PLANES
Large area of copper connected to a circuit’s ground point.
Serves as a return path for current from different components
Reduces electrical noise, interference, crosstalk
..and other functions depending on the circuit
Select Polygon

Type GND
Hit Enter

Select Bottom Layer

Change to 10 mil

Live Demo
Click and follow the edges of the board to form a polygon
The polygon will turn into a dotted line when closed
Use show on the polygon to check that the signal is GND.
(Your GND traces should be highlighted together with the polygon, if it doesn’t, use “NAME” on the polygon to name it as GND. )
Do the same for the Top Layer
Click on Ratsnest to generate solid ground planes

Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
Change to 16 mil

## Slide 31
What goes on to the silkscreen layer?
Top Layer: tPlace(21), tNames(25)
Bottom Layer: bPlace(22), bNames(26)
Dimension
tPlace
tNames
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 32
Making changes to the labels
Select Smash

Select R1

A cross hair for R1 will appear and make R1 editable.
Right Click R1 > Properties
You can now move the Labels as well.
Do the same for the others where required.

Under Size, Select 50

Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 33
Writing text on to silkscreen layer
Select tPlace for Top Layer
Select bPlace for Bottom Layer

Play around with size, ratio and font till happy
(Remember: Ratio only works with Font: Vector!)


Select Text > Write text > Enter
NOTE:
You may choose to have just text, or just an image, or both on the silkscreen layer.
If you’re just placing text, follow the instructions here, and when you’re done, go straight to the last slide.
If you wish to place an image, continue till the last slide.
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes
ALWAYS USE VECTOR FONT

## Slide 34
Preparing your image for silkscreen (Using paint)
Make sure your image is in .bmp Format, Monochrome (1bit)
(If your image is already in Black & White but not in the above format, use Paint to Save As .bmp Monochrome)
WINDOWS USERS
(If you have already done the conversion in PAINT, skip this slide)
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 35
Adding your image into the library
Let’s put your image into the library for easy usage
Under EAGLE’s control panel, Double click on AISCube_BYOG.lbr
The library window will pop up
Select Library > Package
In the textbox next to “New”, Name your image as “Logo” (or whatever makes you happy)
Click OK
A package editor window (that looks like a board layout window) will pop up
Proceed to import bmp (next slide)




Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 36
Import bmp
File > Run ULP
Select import-bmp.ulp
Select your image
Info Box > Click OK
Select Black > OK
Ensure your settings are as follows:
  Format: Scaled
  Unit: MM
  Scale Factor: 0.1
  Layer: 21 (tPlace)
OK > Run Script
Change the Grid to a value like 10mm to check sizing
If you would like to redo the image at a different size, Delete the entire group, and repeat from Step 1 while playing around with the scale factor till you’re happy with the sizing
Once you’re happy with the size, Save the library.
Go to EAGLE’s control panel
Update AISCube_BYOG.lbr (right click> update)
In your board design, Click on ADD > LOGO
Place logo onto board
Preparing the board
Part Placement
Preparing to Route
Power Lines
Signal Lines
Silkscreen Items
Schematic Drawing
GND Planes

## Slide 37
Done!
Please email your entire project folder to
FAZLI@12GEEKS.COM
By Sunday (13/11/2016) Night 2359 hours